## Slide 1: Formal Methods for Safety Critical Control Systems
DAE-BRNS Theme meeting on Verification and Validation of Control Systems
(Feb 17, 2017, Variable Energy Cyclotron Centre, Kolkata)
Pallab Dasgupta
FNAE, FASc
Professor, Dept. of Computer Science and Engg
Dean (Sponsored Research
and Industrial Consultancy)

## Slide 2: Why are formal methods significant in control domain?
Today, safety critical control systems:
  Are designed using CAD tools ( with hidden optimization algorithms )
  Are component based – often from multiple vendors
  Use electronic components ubiquitously
  Are often controlled / monitored in real time using embedded software ( cyber-physical systems )
Examples:
  Aircraft stability
  Electronic braking in automobiles
  Smart Electrical Grids
  Atomic reactors
How to prove that such systems are designed correctly?
A big challenge, but highly recommended in international safety standards
Safety Standards recommending Formal Methods in Verification
Aeronautics (DO-178C)
Automotive (ISO 26262)
Industrial process automation (IEC 61508)
Nuclear (IEC 60880)
Railway (EN 50128)
Space (ECSS-Q-ST-80C)

## Slide 3: Development Cycle of Embedded Control
System Identification
Controller Design
Control System Analysis
Message Scheduling
Task Mapping & Scheduling
Task Partitioning
Code Generation
Timing & Performance Analysis
Are Control Objectives Satisfied?
Equations
Software
NO
System Model
Controller
CONTROL DESIGN PHASE
SOFTWARE DESIGN AND PLATFORM MAPPING PHASE
TESTING PHASE

## Slide 4
PART-1
FORMAL METHODS FOR VERIFICATION OF CONTROL DESIGN

## Slide 5: System Modeling and Verification
Incorrect / Unknown
Revise Design
System Model
Formal Specification
Correct
Verification (algorithmic)
Model of Physical System
Model of Software
System Model
continuous dynamics
x˙ = f (x)
discrete dynamics

## Slide 6: Example: Cooling of a reactor
One or more control rods are inserted between fuel rods
  Controls the neutron flux
  .. that is, the number of neutrons that split further uranium atoms
Keeping them inserted for too long slows down the reactor
Allowing the temperature to rise beyond a level is dangerous
  There exists points of no return – leads to meltdown

## Slide 7: A system with two rods
Three discrete states:
State-1: None of the two rods are in the reactor
State-2: Only Rod-1 is in the reactor
State-3: Only Rod-2 is in the reactor
x  temperature of coolant
Temperature changes in State-1 as per the following equation:
Note that:
When x is above 500, temperature continues to rise
When x is below 500, temperature continues to fall
If the temperature is allowed to fall below 500, the reactor will shut down.

## Slide 8: Effects of control rods
Cooling states:
State-2: Only Rod-1 is in the reactor
State-3: Only Rod-2 is in the reactor
Temperature changes in State-2 as per the following equation:
Temperature changes in State-3 as per the following equation:
Note that:
Rod-1 cannot bring the temperature down if it crosses 560
Rod-2 cannot bring the temperature down if it crosses 600
If temperature crosses 600, meltdown is inevitable
Rod-1 may be inserted when x < 560
Rod-2 may be inserted when x < 600
.. and they have to be taken out sometime when x > 500

## Slide 9: Restrictions on control rods
For mechanical reasons, the rods can be lowered into the core only if it has not been there for at least 20 seconds
Which means:
Both rods may become unavailable at some time
If temperature crosses 600 in the meantime, then consequences are catastrophic
Control problem: Develop a strategy to operate the rods.
Safety validation problem: Prove that meltdown is never possible under any application of that strategy

## Slide 10: Hybrid Automaton (Skeleton)
State-1: No rods
State-3: Rod-1 is in
State-2: Rod-2 is in
x = 510 (Initial condition)

## Slide 11: Introducing constraints on rod movement
For mechanical reasons, the rods can be lowered into the core only if it has not been there for at least 20 seconds
State-1: No rods
State-3: Rod-1 is in
State-2: Rod-2 is in
x = 510 (Initial condition)
c1 = c2 = 20
c1  20
c2  20
c1 := 0
c2 := 0

## Slide 12: First-cut strategy on Hybrid Automaton
Move an available rod in after temperature rises above 550. Remove the rod after the temperature drops to 510 or below.
State-1: No rods
State-3: Rod-1 is in
State-2: Rod-2 is in
x = 510 (Initial condition)
c1 = c2 = 20
x > 550 and c1  20
x > 550 and c2  20
x  510
c1 := 0
x  510
c2 := 0
Is this a safe strategy?

## Slide 13: Success Run of the First-cut strategy
Move an available rod in after temperature rises above 550. Remove the rod after the temperature drops to 510 or below.
Rod Timeout Counters
Reactor Temperature
Point of No-Return
@ 550
Flow Pipe for First-Cut Strategy
This is a safe strategy!
But what about efficiency?
OBSERVE
When either rod’s timer is below 20, the other rod can be inserted at 550.
Beyond a temperature of 550, both Rod’s are ready for insertion if they haven’t already been inserted.

## Slide 14: Second strategy on Hybrid Automaton
Move an available rod in after temperature rises above 550 (for Rod-1) and 590 (for Rod-2). Remove the rod after the temperature drops to 540.
State-1: No rods
State-3: Rod-1 is in
State-2: Rod-2 is in
x = 510 (Initial condition)
c1 = c2 = 20
x > 550 and c1  20
x > 590
x > 550 and c2  20
x  540
x  510
c1 := 0
x  540
x  510
c2 := 0
Is this a safe strategy?

## Slide 15: Second strategy on Hybrid Automaton
Rod Timeout Counters
Move an available rod in after temperature rises above 550 (for Rod-1) and 590 (for Rod-2). Remove the rod after the temperature drops to 540.
OBSERVE
It is possible for both rods to be unavailable for use, while temperatures soar to reach meltdown.
Beyond a temperature of 550, there is a possibility that neither rod can be inserted!
Reactor Temperature
Point of No-Return
@ 550
Flow Pipe for Second Strategy
UNSAFE!

## Slide 16: Failing Run of the Second strategy
State-1: No rods
State-3: Rod-1 is in
State-2: Rod-2 is in
State-1: No rods
State-1: No rods
Move an available rod in after temperature rises above 550. Remove the rod after the temperature drops to 540: FAILS when Rod 2 is placed in @ 590 ; Rod 1 is placed in @ 550
MELTDOWN

## Slide 17
How does the tool find out such counter-examples?

## Slide 18: Verification is proving that bad states are not reachable
State of a hybrid automaton:  Vals of continuous vars, Vals of discrete vars 
Bad states in our example: All states with x > 600
Is any bad state reachable
from any initial state?
INITIAL
STATES
BAD
STATES
State transition system

## Slide 19: States and Transitions of Hybrid Automaton
State of a hybrid automaton:  Vals of continuous vars, Vals of discrete vars 
Bad states in our example: All states with x > 600
Two types of transitions:
Discrete transitions – transitions between the discrete locations of the HA.
  These are instantaneous transitions – no time passes
  For example, a rod is inserted / removed
Time transitions – continuous variables change over time, no change in discrete locations
  For example, temperature rises inside the reactor in State-1

## Slide 20: Discrete and Continuous Successors
Discrete successor states Postd(S)
all x’ for which there exists x ∈ S such that:
  x ∈ G, that is, the guard condition is satisfied
  x’ ∈ R(x) and x’ satisfies the Invariant conditions of the successor location
Time elapse successors PostC(S)
all x’ that can be reached from any x ∈ S such that:
  x’ and all intermediate states in S satisfy the Invariant conditions of S
Inv
– time elapse along straight line can be computed as projection along cone [Halbwachs et al.]
– Time elapse along arbitrary trajectory iff time elapse along straight line (convex invariant) [Alur et al].

## Slide 21: Reachability with LHA [Halbwachs, Henzinger, 93-97]
c
t
i
o
n
p
r
o
e
s
t
o
n
s
n
a
o
r
s
o
f
t
r
s
s
e
3
.
c
o
m
c
c
u
s
p
u
e
t
n
o
c
t
y
b
e
s
p
a
e
e
m
2
t
1. get projection cone
invariant
successors
initial states
derivatives
projection cone
2. time elapse by projection
3. compute successors of transitions

## Slide 22: Fixpoint computation
Fixpoint computation
Initialization: R0 = Ini
Recurrence: Rk+1 = Rk ∪ Postd(Rk ) ∪ Postc(Rk)
Termination: Rk+1 = Rk ⇒ Reach = Rk .
Problems
in general termination not guaranteed

## Slide 23: Reachability by Time-Discretization
Goal:
– Compute sequence k over bounded time [0,Nδ] such that:
Reach[0,Nδ](XIni) ⊆ Ω0 ∪ Ω1 ∪ . . . ∪ ΩN
Approach:
– Refine k by recurrence:
– Condition for :
Reach[0,δ](XIni) ⊆ Ω0
Reach[0,3δ](XIni)
2δ 3δ t
δ
0
0
1

2
Ωk+1
= e Ωk
Aδ

## Slide 24: Time-Discretization with Convex Hull
Overapproximating Reach[0,δ]:
X0
Reach[0,δ](XIni)
X1
Conv(X0, X1)
Bloat(Conv(X0, X1))
Flow Pipe – Reachable Set
If the over-approximated reachable set is free from bad states, then we have formally proven the safety

## Slide 25: Our work in this domain
Proving mixed-signal assertions on hybrid automata
Introducing the notion of formal features
Formal evaluation of features on hybrid automata

## Slide 26: Features: Real valued functions computed over assertion matches
  end
  var t1, t2 ;
  @+(M.Vout ≥ 0.1*Vs) @+(M.Vout ≥0.9*Vs)
  |-> RiseTime = t2 - t1;
,t1= $time
, t2= $time
Rise Time of a second order response of a signal is the time taken for a signal (Vout) to rise from 10% to 90% of its rated value (Vs).
The Assertion: Rise Time should be less than 10ms
  ##[0:10e-3]
Quantitative measurement over a behaviour of a system.
Assertion
Boolean (True/False)
Feature
Real Valued Quantity
  feature RiseTime(Vs);
  begin
  ##[0:$]
The Feature: What is the Rise Time of the circuit?

MinRise <= RiseTime <= MaxRise

## Slide 27
PART-2
A FEW OTHER THINGS

## Slide 28: Tool chains for Safety Critical Control
CONTROL
ELECTRONICS
SOFTWARE
Modeling / simulation
Recent: Formal tools
(PHAVER, SpaceX, Statemate)
Electronic Design Automation
Platform modeling tools
Recent: Formal tools
(VCFormal, JasperGold)
Embedded software testing
Platform emulators
WCET analyzers
Recent: Formal tools
(CBMC, SATABS, Spin)
PROBLEMS:
No integrated development environment
Lack of standardization

## Slide 29: Steps in Design of Software Controlled Systems
CONTROL MODEL
CODE
PLATFORM MAPPING
Control Law is developed using principles of control theory and modeled in platforms like MATLAB
Deployment on
Platform and Testing
Software tasks are developed for interpreting data received from sensors, and interpreting the control law to find the actuation
levels.
Software tasks are mapped to the processors – to be executed periodically within deadlines determined by the control sampling requirement.

## Slide 30: Problems arising out of non-ideality of platform
Software based control samples and actuates at discrete time points
  Sampling rate is decided based on control requirements
The platform is expected to execute the control loop as per the recommended sampling and actuation rate
  In reality this may not happen at all times
    Sensor data may arrive late
    Contention for ECU among multiple control loops

## Slide 31: Two directions in our research
Formal analysis of the effect of loop execution patterns
How does it affect stability
How to design controllers that remain stable under adaptively changing loop execution patterns
Formal analysis of the effect of platform dependent delay patterns on control
Timing aware model based design

## Slide 32: Multiple (Switched) Controller Scheduling
Switched Controller Schedules
  : particular combination of controllers that may execute
  Word , (where each ) specifies a schedule
  Denoting sequence of combinations,
  Sequence of transformations corresponding to this schedule,
Controller-1
Controller-2
Plant
Plant
Switch
Controller-1
Controller-2
Time
Δ 2Δ 3Δ 4Δ 5Δ 6Δ 7Δ 8Δ
Challenge: Compute set of schedules (σ) for which the system is stable

## Slide 33: Control Stability
Asymptotic Stability:
  , or equivalently
  be the composed system state after m timeslots,
  is the initial state, and is the scheduled control at time ti
Stable Modes System Stability:
g1(x)
g2(x)
Switching may introduce instability!

## Slide 34: Exponential Stability
Formal Definition:
For parameters and , a system expressed as, , is said to be -exponentially-stable if for every and .
ω-regular Property: [R. Alur & G. Weiss]
  For and ; the language of exponentially-stable schedules such that any interval of length l is contracting by at least ρ, can be expressed as:
  for every .
  The language of all admissible (exponentially stable) schedules is ω-regular.
Regular
Stability
Exponential Stability
Quantified Version of Stability

## Slide 35: Automata-based Control Schedules
Buchi-Automaton Construction for Language ExpStab(l, ρ)
  Given and , the steps are as follows:
  Construct the inadmissible set,
  Build the regular expression,
  Translate the regular expression to a deterministic finite automaton
  Delete all states from which there is no path to an accepting state

## Slide 36: Automata-based Control Schedules
Example
  System with 2 types of control schedules,
  Inadmissible Set, B = {1112,1121,1211,1212,1222,2111,2121,2122,2212,2221}
  and are stable,
  meaning, and
Figure satisfying the following: for ,

## Slide 37: The AUTOSAFE Project
CONTROL MODEL
CODE
PLATFORM MAPPING
TIMING ANALYSIS
PLATFORM AWARE
CONTROL
ANALYSIS
AUTOSAFE develops the notion of platform aware control analysis
Built-in formal methods guarantee early resolution of timing issues
Tata Research Development and Design Centre (TRDDC)
Technische Universität München,
Real-Time Computer Systems (RCS)
INCHRON GmbH
Our partners in AUTOSAFE

## Slide 38: AUTOSAFE Tool Flow

## Slide 39
NEW INITIATIVES _______________________________________
Under the IMPRINT program of MHRD, we are setting up FMSAFE, a national center on formal methods for safety critical systems, in partnership with IIT Bombay and IIT Kanpur.
We will partner Airbus and Verimag Labs, France on formal methods and tools for verification and analysis of avionic control systems.
In partnership with Synopsys, the world leader in electronic design automation, we are setting up the second phase of the Synopsys CAD Labs for working on some of the most challenging design automation problems.
Other forthcoming initiatives include an Indo-UK consortium project on control strategies for smart electrical grids, and participation in a project on hybrid electric vehicles.

## Slide 40
Integrated
Circuits
Automotive
Control
Railway
Signaling
INDUSTRY PARTNERS
Network
Access
Control
Avionic
Software
Power Grids
Modeling Formalisms
Software Verification
Verification of Control Systems
PROFILE
12 PhDs graduated, 9 ongoing
170+ research papers, 3 books
Decision Procedures
Hardware Verification
Performance verification
  Power, Reliability, Timing
We prove the safety of tomorrow’s designs !!
Contacts:
  Pallab Dasgupta: pallab@cse.iitkgp.ernet.in
  Soumyajit Dey: soumya@cse.iitkgp.ernet.in