## Slide 1
Micro-architectural Attacks:
Where Security meets
Computer Architecture
Debdeep Mukhopadhyay
Professor
Secured Embedded Architecture Laboratory (SEAL)
Department of Computer Science and Engineering
IIT Kharagpur
debdeep@cse.iitkgp.ac.in
debdeep.mukhopadhyay@gmail.com

## Slide 2: Software and Hardware
Computer hardware are the physical parts or components of a computer, such as the central processing unit, monitor, keyboard, computer data storage, graphic card, sound card and motherboard.
Software comprises of instructions that can be stored and ran by hardware.
Are they related?
Or are they two different
Disciplines?

## Slide 3: Two sides of the “computation coin”
This seemingly disparate sub-disciplines of computer science, software and hardware, are intrinsically related.
Though in many schools there is an explicit marked separation and the single subject is organized for pedagogy and research as:
  Computer Science
  Computer Engineering

## Slide 4: Micro-architectural Attacks: Design for Security
To quote Bruce Schneier, “Fixing them either requires a patch that results in a major performance hit, or is impossible and requires a re-architecture of conditional execution in future CPU chips. It shouldn't be surprising given that microprocessor designers have been building insecure hardware for 20 years. What's surprising is that it took 20 years to discover it."
Reference: Spectre and Meltdown, Daniel Gruss, Moritz Lipp, Yuval Yarom, Paul Kocher, Daniel Genkin, Michael Schwarz, Mike Hamburg, Stefan Mangard, Thomas Prescher and Werner Haas, Google Ground Zero Project
Computer Architecture has been designed with performance as a primary design criteria.
Security has been an after thought.
For example:
Speculative execution is an optimization technique where a computer system performs some task that may not be needed.
This has been the basis of the recently discovered attacks: Spectre and Meltdown.

## Slide 5: Timing Channels in Cryptography due to Cache Memories
Bob
(Cipher)
Alice
(Adversary)
Monitor Time
Secret
Key
Microprocessor
Main Memory
Cache Memory
If there is a Cache Hit
  Access time is less
If there is a Cache Miss
  Access time is high
Why is “time” a channel for Information Leakage?
Adversary wants to get Bob’s secret key

## Slide 6: Time-Driven Cache Attack Principle
  If cache hit (less time) :
Table
Table
  If cache miss (more time):
(Adversary)
Part of a Cipher
P0
,P4
Notes: Sbox is generally implemented as a table
6

## Slide 7: Classes of Cache Attacks
Three ways to identify cache behavior
Cache Trace Attacks
Cache Access Attacks
Cache Timing Attacks

## Slide 8: Cache Trace Attacks
The Power Profile of the system gives away cache behavior.
Without Cache Miss
With Cache Miss

## Slide 9: Cache Access Attacks : Osvik’s Attack
Uses a spy program to determine cache behavior
Microprocessor
Spy
AES
Memory
Cache Memory
Part of the cache memory occupied by tables
Cache Miss
Cache Hit

## Slide 10: Cache Timing Attack
Based on measuring the total time for encryption.
Used to attack a remote server.
Server running Encryption Software
Remote Attacker
Network
Trigger Encryption &
Measure time taken

## Slide 11: Bernstein’s Cache Timing Experiment
AES
Random
P0 = 00 - FF
Cipher Text
Characteristic of Plaintext Byte P0
(Deviation from mean time)

## Slide 12: Bernstein’s Cache Timing Attack
Put key to all ZEROs and perform experiment
12
Repeat experiment with unknown key
Correlate the two results

## Slide 13: Why Cache Attacks Work on AES
The AES Structure
  Add initial Key
  Nine Rounds of
    Byte Substitution
    Shift Row
    Mix Column
    Add Round Key
  Final Round
    Byte Substitution
    Shift Row
    Add Round Key
Substitute 16 bytes from a 256 byte lookup table
Chester Rebeiro, Mainack Mandal, Debdeep Mukhopadhyay, "Pinpointing Cache Timing Attacks on AES", VLSID 2010,

## Slide 14: Software Implementations of AES(OpenSSL)
Merges all round operations into 4 lookups. Uses 4 tables T0, T1, T2, T4 , each of size 1024 byte.

## Slide 15: Software Implementations of AES(OpenSSL) (contd.)
Since AddRoundKey can be implemented by additional 32 bit XOR, AES round can be implemented with 4 kB of tables, with 4 table look ups and one XOR per column per round.
Note that final round does not have a Mixcolumn step.
Each table has 256 entries of size 4 bytes. Thus each table is of 1 kB.

## Slide 16: Software Implementations of AES (OpenSSL)

## Slide 17: AES Execution Time for 4KB Table
Cache Attack works because of varying execution time.
Since, Nt = Nm + Nh

## Slide 18: AES Execution Time with 256Byte Table
  …… Encryption Time is a constant
Cache Attacks
believed to be difficult

## Slide 19: Osvik’s Attack on AES-with 256B Table
Won’t Work!!!
Microprocessor
Spy
AES
Memory
Cache Memory

## Slide 20: Bernstein’s Attack on Small Tables
Large
Tables
Small
Tables
Lesser deviations in Encryption Time

## Slide 21: Some Opinions on Cache Timing Attacks
[Kelsey. et.al., 2000, Section 7]
“We believe attacks based on cache hit ratio in large Sbox ciphers like Blowfish, CAST and Khufu are possible”
We now show that cache attacks are possible even on ciphers with small sboxes
Chester Rebeiro, Debdeep Mukhopadhyay, Junko Takahashi and Toshinori Fukunaga, "Cache Timing Attacks on Clefia", Indocrypt 2009.

## Slide 22: Analysis of Cache Timing Attacks
Processor’s aim : Reduce the miss penalty
Techniques used to achieve this are
  Speculative Loading
  Prefetching
  Out-of-order loading
  Parallelization
  Overlapping

## Slide 23: Speculative Loading
Speculative Loading :Loading of data into processor before preceding branches are resolved.
  Effect on Cipher Execution :None, since branches are generally not used in block ciphers.

## Slide 24: Out-of-Order Loading
Data accessed in an order not strictly specified by the program.
LOAD AX, #1000
LOAD BX, #2000
LOAD CX, #3000
LOAD DX, #4000
LOAD DX, #4000
LOAD BX, #2000
LOAD AX, #1000
LOAD CX, #3000
Program
Execution

## Slide 25: Out-of-Order Loading on a Cipher
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
Round 1
Round 2
Out of order loading works only within a round & not between rounds.

## Slide 26: Parallelization & Overlapping
Parallelization : Two or more cache misses are serviced simultaneously.
Overlapping : Memory reads are pipelined.
Effect on Cipher Execution :
Consider a 5 round block cipher with 4 misses
Time(E1) < Time(E2)
2 misses
1 miss
1 miss
0 misses
0 misses
1 miss
1 miss
1 miss
0 misses
1 miss
E1
E2

## Slide 27: Extending Cache Timing Attack to Work on Small Table Ciphers
Challenges:
1. The deviation in encryption time is too less.
2. Timing measurements need to be more accurate.

## Slide 28: Improvements to the Timing Attack (1)
Improving Timing Measurements
  Use ‘RDTSC’ instruction to measure timing.
    This is prone to errors due to processor pipeline and out-of-order execution.
  Also use ‘CPUID’ before calling RDTSC
    This flushes the processor pipeline.
    Hence all RDTSC instructions done on a fresh pipeline.

## Slide 29
Vary only those bytes which go to the same sbox as P0.
S1
XOR
P0
K0
S2
XOR
P1
K1
S1
XOR
P2
S2
XOR
P3
K3
K2
AES
Random
P0 = 00 - FF
Constant
Improvements to the Timing Attack (2)

## Slide 30: Attack on CLEFIA
CLEFIA is a block cipher designed by Sony Corporation
It has small tables of 256 bytes.
There are 18 rounds in the cipher
  each round has 8 look-ups
  there are 2 S Boxes of 256 bytes
  Thus there are 4 look-ups per S-box in each round.

## Slide 31: CLEFIA Attack Results
On Intel Core 2 Duo, the first phase of the attack takes 1300 seconds,
Second phase (with secret key) takes 312.5 seconds
The attack has also been tested successfully on
Pentium 4
Intel Atom
Xeon – Core 2 Server
The attack fails on Pentium 3
Chester Rebeiro, Debdeep Mukhopadhyay, Junko Takahashi and Toshinori Fukunaga, "Cache Timing Attacks on Clefia", Indocrypt 2009.

## Slide 32: Correlation Results on CLEFIA
32

## Slide 33: Part-III
Looking into Micro-architecture Attacks
: An Ideal Implementation for Cache Timing Attacks
Chester Rebeiro, Debdeep Mukhopadhyay:Micro-Architectural Analysis of Time-Driven Cache Attacks: Quest for the Ideal Implementation. IEEE Trans. Computers 64(3): 778-790 (2015)

## Slide 34: Ideal Implementation against Time-Driven Cache Attacks
T
P0
K0
T
P4
K4
Block Cipher
Random
P0
Cipher Text
P4
  Suppose
  (K0 = 00 and K4 = 50)
P0 = 0, all other inputs are random
Make N time measurements
Segregate into Y buckets based on value of P4
Find average time of each bucket
Find deviation of each average from overall average (DOM)
P4 | Average Time | DOM
00 | 2945.3 | 1.8
10 | 2944.4 | 0.9
20 | 2943.7 | 0.2
30 | 2943.7 | 0.2
40 | 2944.8 | 1.3
50 | 2937.4 | -6.3
60 | 2943.3 | -0.2
70 | 2945.8 | 2.3
: | : | :
F0 | 2941.8 | -1.7
Average : 2943.57
Maximum : -6.3

## Slide 35: Different DOM for Different Implementations
Implementation | Difference of Means
AES (OpenSSL 0.9.8a ) | -6.5
DES (PolarSSL 1.1.1 ) | +11
CAMELLIA (PolarSSL 1.1.1) | 19.2
CLEFIA (Ref. Implementation 1.0) | 23.4
Easiness to attack

## Slide 36: Effect of Micro-architecture in Cache Memory in Superscalar Processors
Assume the cache is clean before executing a snippet
Snippet A
Snippet B
Snippet A !!!
Which is faster?
In Superscalar processors cache misses can be
pipelined and parallelized provided there are no memory
dependencies

## Slide 37: Which Implementation is Faster in a Superscalar Processor?
Snippet B
Snippet A
Cache misses in Snippet A can be
pipelined and parallelized
time
time

## Slide 38: Memory Access in a Cipher
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
Round 1
Round 2
Round 1
Round 2
In a cipher, memory accesses within a round can
be parallelized and pipelined. But memory accesses
across rounds should be serialized
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T

## Slide 39: A Model for Block Cipher Implementations
Table Accesses

## Slide 40: Ideal Implementation
Ideal
Table size influences
the DOM
(such as in AES)
Micro-architectural features have a high influence on DOM
(such as in CLEFIA)
Chester Rebeiro, Debdeep Mukhopadhyay:Micro-Architectural Analysis of Time-Driven Cache Attacks: Quest for the Ideal Implementation. IEEE Trans. Computers 64(3): 778-790 (2015)

## Slide 41: Average Cache Misses per Round (mr)
Mathematical Model
Access/Round
Size of Tables
Round Number
Cache Line Size
Average
Cache Misses for the round

## Slide 42: Average Time for Encryption
Average time for Round 1
Average time for Round 2
Average time for Round 3
Average time for Round 4
Average time for Last Round
Total time for Encryption

## Slide 43: Comparing Cipher Implementations
Test Platform :
  8 core Intel Xeon 2.13GHz
  Depends on the executing core
Cipher Implementations
  AES - OpenSSL (0.9.8ka)
  DES - PolarSSL (1.1.1)
  CAMELLIA - PolarSSL (1.1.1)
  CLEFIA – Reference Code of Sony (1.0)

## Slide 44: Different Avatars for Clefia

## Slide 45: Practical Validations
Success of the Attack vs Number of Measurements Made
Implementations identified by
the mathematical model
are more difficult to attack

## Slide 46: More Experiments
With CLEFIA and CAMELLIA on different platforms
Test platform E5606: Intel 8 core Xeon 2.13GHz, running Ubuntu 12.04
Test platform E5345 : Intel 4 core Xeon 2GHz, running Fedora OS

## Slide 47: Two Sources of Leakage
In superscalar processors there are two sources of leakage
  Leakage due to cache misses has a negative effect
  Leakage due to micro-architectural features has a positive effect
Ciphers can be designed so that the two leakages cancel each other
This allows building implementations more protected against time-driven cache attacks

## Slide 48: Patent

## Slide 49: Part-IV
Modern Times:
Timing Attacks in Modern Systems

## Slide 50: Timing Attack in Modern Systems
In modern day systems timing attack faces difficulties because of the modifications for performance improvements.
Timing measurements for the execution of a same instruction with RDTSCP creates different timing values at different instances.
New RDTSCP benchmark code generates similar timing measurements.

## Slide 51: Timing Attack in Modern Systems
Nondeterminism
(performance improvements)
Requires ROOT ACCESS
Can be done from USER space
disable
disable
eliminate
disable

## Slide 52: Timing Attack in Modern Systems
How to Benchmark Code Execution Times on Intel® IA-32 and IA-64 Instruction Set Architectures - Gabriele Paoloni (White Paper)
Removes all Nondeterminism
(with root access)

## Slide 53: Timing Attack in Modern Systems
Spy thread
while(1){;}
Virtual Core 0
Virtual Core 1
Time measurement thread
start = time_fn()
/*function*/
end = time_fn()
timing = end - start
Core
Spy thread keeps one virtual core occupied and lets other thread run solely on other virtual core
Eliminate nondeterminism due to hyper-threading from user space

## Slide 54: Timing Attack in Modern Systems
Accuracy around 60%
After Removing all Indeterminism
Accuracy 0%
Timing Attack on Modern System (Core i5)

## Slide 55: Timing Analysis for Row Hammering
Cache Miss
Crypto execution
Cache Memory
DRAM

## Slide 56: Timing Analysis for Row Hammering
Rank
Banks
Rows
Slice 0
Slice 1
Slice 2
Slice 3
DRAM access on cache miss
Copies data to indexed cache set and slice

## Slide 57: Timing Analysis for Row Hammering
Slice 0
Slice 1
Slice 2
Slice 3
Rank
Banks
Rows
Once data in cache, access to same data results in Cache Hit
Next access results in Cache Miss
Access to DRAM on cache misses imposed by spy
Concurrent accesses to DRAM banks to enforce rowbuffer collision
Spy fills the cache sets with its own data

## Slide 58: New Frontiers of Micro-Architectural Attacks
.
Bypass existing Address Space Layout Randomization schemes by exploiting a side-channel created through shared BTB
Jump over ASLR
CacheBleed
Targets OpenSSL 1.0.2f RSA modular exponentiation on Intel processors using cache bank conflict

## Slide 59: New Frontiers of Micro-Architectural Attacks
Exploiting Speculative Execution
Spectre: uses branch misprediction and out-of-order execution to access unprivileged data.
01
03
Foreshadow: uses L1TF and page fault along with meltdown to retrieve data across SGX enclaves.
02
Meltdown: uses out-of-order execution and prime-probe method to access kernel pages

## Slide 60: Conclusions
Micro-architectural attacks encompasses the intersection of architecture and computer security.
Architectures have been developed to enhance performance:
  Cache memories
  Prefetchers
  Out of order execution
However leakage due to architecture is not yet a guideline for design.
More attacks are emerging and security is getting to be a game changer: Design-for-Security along with other objectives like performance, power, energy.
  Good time to think of clean paper designs for secured computer architecture
  RISC-V is a good open source platform to experiment.

## Slide 61: Thank You for your attention!!
Ref: Viewpoint, By Leah Hoffmann Communications of the ACM, June 2018, Vol. 61 No. 6, Pages 104-ff10.1145/3204453 .

## Slide 62
Please visit us at: https://www.isical.ac.in/~space2019/index.html
Proceedings in Springer LNCS

## Slide 63: Textbook on Hardware Security
"… an excellent job introducing the field of hardware security. It is a good source for upper undergraduates, postgraduates, and practitioners. The book does not need to be read cover to cover, and a select subset of chapters can form an undergraduate or graduate course in hardware security. … an excellent reference and can help graduate students move quickly to the frontiers of research. With its 432 references, the book helps direct readers who want to explore a specific topic in more detail."
—Computing Reviews, April 2015
Mentioned in the global bestseller list for 2015:
http://reviews.libraryjournal.com/2015/05/best-sellers/computer-science-may-2015-best-sellers/

## Slide 64: Text Book on Timing Attacks
Discusses various timing attack algorithms in detail allowing readers to reconstruct the attack.
Presents the application of timing attacks on remote systems and cloud environments.
Examines information leakage models that would help quantify leakage in a covert timing channel

## Slide 65: Text Book on Fault Attacks
Reviews exhaustively the recent key research into fault tolerant architectures in hardware security and cryptography software
Discusses the latest fault attacks on a wide variety of cryptographic implementations, such as biased fault attacks, algebraic fault attacks, and attacks on authenticated encryption based ciphers
Offers hands-on and practical demonstrations for handling complex secure cryptographic architectures, complementing the theoretical analysis

## Slide 66: MOOC Course on Hardware Security
https://www.youtube.com/watch?v=xwgecIX3E4I&list=PLbRMhDVUMngfulSvKL0cT-tn8ULtERsWk&index=1