## Slide 1
Course Name: Hardware Security
Faculty Name: Prof Debdeep Mukhopadhyay
Department : Computer Science and Engineering
Topic
Lecture 26: Power Analysis-II

## Slide 2
Concepts Covered:
Difference-of-Mean (DOM) Method
DOM on AES
Selection Function
DOM on actual power traces on AES, DES, 3-DES
Summary of DOM

## Slide 3
DPA Procedure for AES
1. Make power consumption measurement of about 1000 AES operations, 100000 data points / curve, (Ciphertexti, Curvei)
2. Assume a key for an S-box of last round
3. Calculate last round S-box first bit output for each ciphertext using the assumed key
4. Divide the measurement into 2 groups (output 0 and 1)
5. Calculate the average curve of each group
6. Calculate the difference of two curves
7. Assumed correct key → spikes in the differential curve
8. Repeat 2-7 for other S-boxes
Exhaustive search for 8 bits of key.

## Slide 7: Difference-of-Mean (DOM) Method
DPA selection function : D(C,b,Ks) is defined as computing the value of the
  bth output bit, depending upon
    C: Ciphertext
    KS is the guessed key (6 bits) for the S-Box
Note: If Ks is incorrect evaluating D(…) gives the correct bit in half of the cases for each of the ciphertexts.

## Slide 8: DOM (Contd.)
Attacker obtains m encryption operations and capture power traces, T1..m[1..k], with k sample points each.
An attacker records the m ciphertexts
No knowledge of the plaintext is required

## Slide 9: DOM (Contd.)
T[1][1]
T[2][1]
T[m][1]
T[m][2]
T[2][2]
T[1][2]
T[1][k]
T[2][k]
T[2][k]
Sample Points
C
I
P
H
E
R
T
E
X
T
S
Tabular representation of power traces.

## Slide 10: The Selection Function D
Shift
Rows
Add
Round Keys
+

## Slide 11: The Selection Function D
Sub Bytes and Shift
Rows
Add
Round Keys
+
??
C10
Guess k*

## Slide 12: DPA Mathematically
Attacker now computes a k-sample differential trace ΔD[1..k] by finding the difference between the average of the traces for which D(…) is one and the average for which D(…) is zero.
Principle: If Ks is wrongly guessed, D behaves like a random guess.
Thus for a large number of sample points, ΔD[1..k] tends to zero. But
if its correct, the differential will be non-zero and show spikes when
D is correlated with the value being processed.

## Slide 13: DPA Results - DES
SBOX – 3 BIT – 3 TRACE COUNT = 4,000
2D Differential Plot

## Slide 14: DPA Results - DES
SBOX – 3 BIT – 3 TRACE COUNT = 4,000
3D Differential Plot


## Slide 15
DPA Results - Triple-DES
SBOX – 4 BIT – 2 TRACE COUNT = 10,000
3D Differential Plot


## Slide 16: DPA Results - AES

SBOX – 11 BIT – 8 TRACE COUNT = 15,000
3D Differential Plot

## Slide 17
Summary of the DOM based Differential Power Analysis

## Slide 18
D. Stinson, Cryptography: Theory and Practice, Chapman & Hall/CRC
Lawrence C. Washington, Elliptic Curves: Number Theory and Cryptography, Chapman & Hall/CRC
Jeffrey Hoffstein, Jill Pipher, Joseph H. Silverman, An Introduction to Mathematical Cryptography, Springer.

## Slide 19
Conclusion:
DPA works because of the dependence of power consumption on state bits.
DPA works because of the fundamental way of computation
We discussed about DOM Method.
We applied DOM to a Toy cipher
Applying DOM for AES.