## Slide 1
Course Name: Hardware Security
Faculty Name: Prof Debdeep Mukhopadhyay
Department : Computer Science and Engineering
Topic
Lecture 06 : Hardware Design for Finite Field Inverse

## Slide 2
Concepts Covered:
Multiplicative Inverse in GF(2m)
Itoh-Tsujii Inversion Algorithm
Generalization of Itoh-Tsujii
Hardware Design of Itoh-Tsujii
Performance of the Hardware Circuit

## Slide 3: Multiplicative Inverse
Given an element ‘a’, find a-1 in the field such that a.a-1 = 1.
Techniques
  Extended Euclid’s Algorithm
  Fermat’s Little Theorem
Fermat’s Little Theorem is more efficient on hardware than the Euclidean technique.
Fermat’s Little Theorem
  a-1 = an-2 mod n
  For example 3*3(5-2) mod 5 = 3*2 mod 5 = 1

## Slide 4: Euler's Totient function
Suppose a≥1 and m≥2 are integers. If gcd(a,m)=1, then we say that a and m are relatively prime.
The number of integers in Zm (m>1), that are relatively prime to m and does not exceed m is denoted by Φ(m), called Euler’s Totient function or phi function.
Φ(1)=1

## Slide 5: Example
m=26 => Φ(26)=12
If p is prime, Φ(p)=p-1
If n=1,2,…,24 the values of Φ(n) are:
  1,1,2,2,4,2,6,4,6,4,10,4,12,6,8,8,16,6,18,8,12,10,22,8
  Thus we see that the function is very irregular.

## Slide 6: Fermat’s Little Theorem and Finite Field Inverse
If gcd(a,m)=1, then aΦ(m)≡1 (mod m)
If m=p, is a prime number, thus ap-1≡1 (mod p)
For the field GF(2m), thus we have:

## Slide 7: Addition Chain
Naïve method would require (m-1) squarings and (m-2) field multiplications.
Since, multiplication is costly we don’t apply this method.
Itoh-Tsujii algorithm reduces the number of field operation by using an addition chain for (m-1).
Addition Chain for a positive integer n is a sequence of natural numbers U=(u0,u1,…,ul), st. the following are satisfied:
Example: addition chain for 162, U=(1,2,4,5,10,20,40,80,81,162)

## Slide 8: Itoh-Tsujii Algorithm
For , let
Thus,
Interestingly, can be efficiently computed using recursions:

## Slide 9: Example for m=233
We need to find a-1 = a2m-2 for m=233
We first define an addition chain for m – 1
  (1,2,3,6,7,14,28,29, 58,116, 232)
Then, define βk= a2k-1 then a-1 = (a2232-1)2 = (β232)2
Also define the recursion βk+j= (βk)2jβj
F.R.Henríquezez et. al., A Fast Implementation of Multiplicative Inversion Over GF(2m), ITCC ’05:

## Slide 10: Computing the Inverse of ‘a’
In all we need 232 squarings and 10 multiplications.

## Slide 14: Circuit to Raise Input to Power of 2k
Number of squarings at a stage can be as high as ui/2
  A naïve way would require ui/2 squarings at each step.
Circuit cascades us squarers, where us is an element in the addition chain.
If number of squarings required is less than us, a multiplexer is used to tap out interim outputs.
  In this case, the output is obtained in one clock cycle.
If the number of squarings is more than us, the output of the squaring block is fed back to get squares which are multiples of us. This would require clock cycles.

## Slide 15: Estimating the number of clock cycles
The (l-1) term is due to (l-1) multiplications, assuming one clock cycle for each.
The summation terms are for the squarings at each steps: note, that the number of squarings required are proportional to (ui-ui-1).
The extra clock cycle is for the final squaring operation.

## Slide 16: Quad Circuits vs Squarers
Comparison for LUTs required for Squarer and Quad for GF(29)

## Slide 17: Using Quads Instead of Squarers
On an FPGA, Quads have better LUT utilization compared to squarers.
Delay of a quad and a squarer is the same
Therefore one can use a Quad Itoh-Tsujii algorithm which uses quad circuits instead of squarers.

## Slide 18: Generalisation of Itoh-Tsujii

## Slide 19: Justification
Case 1: When n divides (m-1):
Case 2: When n does not divide (m-1):

## Slide 20: Quad Itoh Tsujii Algorithm
We now require 115 quads (instead of 232) and 9 multiplications. We save 7 clock cycles.
We set n=2
Initial Pre-computation:
To compute the cube, the multiplier is used for 2 clock cycles. Remember there is no squarer.
Likewise, the final squaring also is done by a multiplication step.
So, in total 12 multiplications.

## Slide 21: Estimating the number of clock cycles
#Multiplications: l-2+3=l+1. Note that 2 multiplications are needed initially for pre-computation, and one for final squaring.
Difference in clock cycle:
This can be as high as (m-1)/2 for GF(2m)